## Slide 1: Measure Descriptions for Low Tidal Volume Ventilation
AHRQ Safety Program for Mechanically Ventilated Patients
AHRQ Pub. No. 16(17)-0018-36-EF
January 2017

## Slide 2: Learning Objectives
After this session, you will be able to—
Collect and enter low tidal volume ventilation (LTVV) data using the LTVV Data Collection Tool
Understand the definitions of the data elements
Locate the necessary data elements

## Slide 3: LTVV: Key Interventions
Use multidisciplinary and coordinated approach
Prevent acute respiratory distress syndrome (ARDS)
Use positive end-expiratory pressure (PEEP) ≥ 5 cm H20, not zero end-expiratory pressure
Maintain plateau pressure at ≤ 30 cm H20
Use tidal volume of 6-8 cc/kg predicted body weight (PBW) for patients without ARDS, 4-6 cc/kg PBW for patients with ARDS

## Slide 4: Data Collection
Drives quality improvement efforts
Can be used for quality improvement processes or for research
Provides quantifiable measures of care practices
Guides patient safety conversations
Justifies resource allocations
  Human resources (time)
  Financial resources (money)
  Supplies and equipment (stuff)

## Slide 5: LTVV Data Collection Tool
Intubation
Ventilator mode
Height/gender
Tidal volume (target and actual)
Plateau pressure
PEEP
ARDS status

## Slide 6: Data Collection: Intubation and Ventilator Mode

## Slide 7: Let’s Begin…
Fill out for all beds
Track by bed, not by patient
Include bed number (even if empty)
Is the patient currently receiving mechanical ventilation?
  Y = Patient is currently intubated/trached AND mechanically ventilated
  N = Patient is treated with noninvasive ventilation OR patient is NOT currently intubated/trached AND mechanically ventilated
  E = Empty bed

## Slide 8: Ventilator Modes – Volume-Cycled Modes
Circle 1 for volume-cycled modes
  Assist control
  Synchronized intermittent mandatory ventilation
  Volume support
  Pressure-regulated volume-controlled
  Continuous mandatory ventilation

## Slide 9: Ventilator Modes – Pressure-Cycled Modes
Circle 2 for pressure-cycled modes
  Pressure support
  Continuous positive airway pressure
  Airway pressure release ventilation (APRV)
  Bilevel ventilation

## Slide 10: Ventilator Modes – Other Modes
Circle 3 for other modes
Proportional assist ventilation
Adaptive support ventilation
High-frequency oscillatory ventilation
Extracorporeal membrane oxygenation
Other

## Slide 11: For Vent Modes 1 and 2 Only
Enter patient’s height in either centimeters OR inches
Circle patient’s gender
Enter the target tidal ventilation based on predicted body weight (PBW)
  PBW can be found on the LTVV Quick Cards included in the LTVV data collection tool
Enter the actual tidal volume at the time of observation in the next column
If the ventilator is in a volume-cycled mode, use the preset/prescribed tidal volume
If the ventilator is in a pressure-cycled mode, enter the approximate expired tidal volume

## Slide 12: For Vent Modes 1 and 2 Only
What is the plateau pressure at or nearest to the time of observation?
  If plateau pressure is not available or not known, enter NK
  For APRV/bilevel modes, this is the Phigh value
What is the PEEP at or nearest to the time of observation?
  If PEEP is not available or not known, enter NK
  For APRV/bilevel modes, this is the Plow value

## Slide 13: Data Collection: ARDS

## Slide 14: For ALL Vent Modes (1, 2, or 3)
Does the patient have a risk factor for ARDS?
  Circle Y if the patient has one of the following:
    Pneumonia
    Sepsis, severe sepsis, or septic shock, not secondary to pneumonia
    Aspiration
    Trauma
    Other risk factor
  Otherwise, circle N
Does the patient have a diagnosis of ARDS at the time of observation?
  Circle Y if the patient has a diagnosis of ARDS at the time of observation
  Otherwise, circle N

## Slide 15: Data Measures Guide
Data should drive all quality improvement efforts…
The Data Measures Guide provides detailed instructions on how to calculate and evaluate process and outcome measures in your unit using data gathered from the data collection tools provided for this safety program. The guide can be found on the AHRQ Web site here.
LTVV compliance rates (≥4 and ≤8 mL/PBW) for all patients
LTVV compliance rates (≥4 and ≤6 mL/PBW) for patients with ARDS
LTVV compliance rates (≥6 and ≤8 mL/PBW) for patients without ARDS
PEEP compliance rates (≥ 5 cm H20)

## Slide 16: Questions?